## Slide 1: Logic Gates
Photocopiable/digital resources may only be copied by the purchasing institution on a single site and for their own use
© ZigZag Education, 2021

## Slide 2: Logic Gates
Logic gates are the fundamental building blocks of digital circuits.
© ZigZag Education, 2021
There are three main logic gates:
The NOT gate reverses the input, so if 1 is inputted into a NOT gate it will output 0.
The AND gate will only output 1 if both inputs are 1, otherwise the output will be 0.
The OR gate will output 1 if either or both of the inputs are 1.
1
0
1
1
1
1
0
1
AND
NOT
OR

## Slide 3: Additional Gates
There are some additional logic gates you need to know about.
© ZigZag Education, 2021
Exclusive OR - Only outputs a 1 if one of the inputs is 1 (not both).
This is equivalent to an OR gate followed by a NOT gate.
This is equivalent to an AND gate followed by a NOT gate.
0
1
0
0
0
1
XOR
NOR
NAND
1
1
0

## Slide 4: Combining Gates
Logic gates can be combined in order to create logic circuits.
© ZigZag Education, 2020
For example:
1
0
1
0
1
0
0
1

## Slide 5: Truth Tables
All the possible outcomes of a logic diagram can be represented using a truth table.
© ZigZag Education, 2021
We start by filling in all the possible combinations of inputs.
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 6: Another Example
Here is another example of a truth table for a logic diagram consisting of two logic gates.
© ZigZag Education, 2021
A | B | X | Y
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A
B
X
Y

## Slide 7: Logic Statements
Logic diagrams can also be written as logic statements.
© ZigZag Education, 2021
This logic statement shows that C is 1 if either or both A and B are 1.
C = A OR B
We can also combine Boolean operators to create more complex logic statements.
C = NOT(A OR B)
In this case the NOT operator is applied to the output of A OR B, meaning it is reversed.

## Slide 8: Scenarios (1)
You may be asked to produce a logic diagram for a given scenario.
© ZigZag Education, 2021
A system is used to monitor athletes while they are training.
A heart rate (H) monitor is used to monitor the athlete’s heart rate.
An oxygen (O) is used to monitor the athlete’s oxygen levels.
An alarm (A) is sounded if both the heart rate (H) and oxygen (O) readings are outside safe limits.
Example Scenario
H
O
A

## Slide 9: Scenarios (2)
You could also be asked to produce a truth table for a logic statement that relates to a specific scenario.
© ZigZag Education, 2021
INPUTS |  | OUTPUT
H | O | A
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
H
O
A

## Slide 10
END